## Slide 1: Digital Clock Kit University of Autodidact- Soldering 101

## Slide 2: Please Do Not Get Ahead of Instructions!

## Slide 3: Please keep the Soldering Iron and work on the provided matt to protect tables.

## Slide 4: Soldering Iron Temperature Setting:

## Slide 5: Set for about 325 to 350 Celsius

## Slide 6: Please Use Caution! Iron Is HOT! It Will Burn!!

## Slide 8: Gently empty contents on table.. Use Caution – very small parts!

## Slide 9: Unfold directions and read thoroughly!

## Slide 10: Organize parts within reach but off to side..

## Slide 11: Grab PC Board, with component side up

## Slide 12: Locate the 4.7K ohm resistors (5 total)

## Slide 16: Grab one 4.7k resistor and shape legs

## Slide 17: Place first Resistor in spot labeled “R1”

## Slide 18: Flip PC board over and fold legs just slightly **ensure resistor is flat against board**

## Slide 19: Set board down and begin first solder joints

## Slide 20: Grab wire cutters and remove excess legs after soldered.

## Slide 21: Example of a clean cut and good solder joint..

## Slide 22: Grab another resistor in place it in “R3”

## Slide 23: Solder, then cut legs on R3

## Slide 24: Grab another resistor in place it in “R4”

## Slide 25: Solder and Cut excess on R4

## Slide 26: Grab another resistor and place in “R5”

## Slide 27: Solder and cut excess on R5

## Slide 28: Grab the last resistor and place in “R6”

## Slide 29: Solder and cut excess of R6

## Slide 30: Locate the two 1n4007 diodes

## Slide 31: Diodes only allow flow in one direction!

## Slide 32: Place on diode in spot “D1”

## Slide 33: Solder and cut excess on D1

## Slide 34: Grab 2nd diode and place in spot “D2”

## Slide 35: Solder and cut excess on D2

## Slide 36: Locate the two ceramic capacitors (30p) as seen on the left here

## Slide 37: Ceramic capacitors are typically non-polorized

## Slide 38: Place one of the 2 ceramic capacitors marked “30” in spot “C2”

## Slide 39: Solder and then cut excess of C2

## Slide 40: Grab the other ceramic capacitor marked ‘30’ and place it in spot “C3”

## Slide 41: Solder C3 and cut excess leads

## Slide 42: Located last ceramic capacitor which is marked ‘104’ and place it in spot ‘C5’

## Slide 43: Ceramic Capacitor for location ‘C5’

## Slide 44: Solder and cut excess of C5

## Slide 45: Locate the Transistor

## Slide 46: Orientation of legs is crucial – magic smoke can be permanently released if a mistake is made!

## Slide 47: Place transistor in spot Q1 as shown…

## Slide 48: Solder Q1 and then trim excess legs

## Slide 49: Locate the 12khz Crystal

## Slide 50: The Crystal is the ‘heartbeat’ of the circuit. It regulates a pulse so that the clock keeps correct time.

## Slide 51: Place the crystal in location ‘T1’

## Slide 52: Solder and then cut excess leg on the crystal

## Slide 53: Remove tape from this thing-a-ma-jig

## Slide 54: You end up with 2 pieces. One is an IC – Integrated Circuit, and the other is a socket for it.

## Slide 55: simple diagram of a integrated circuit

## Slide 56: Inside a integrated circuit (IC)

## Slide 57: Orientation is critical for IC’s

## Slide 58: Grab the IC socket (not the IC) and place it on PC board spot “U1” **Note the orientation!

## Slide 59: Do Not place IC in socket yet

## Slide 60: Locate the Resistor Array

## Slide 61: This is a typical schematic of a resistor array but ours we have here is not typical… ours here is orientation critical.

## Slide 62: Notice the white dot on left side which indicates ‘pin one’ on our specific part. Pin one goes to the left on PC board as seen in the little square.

## Slide 63: Insert the resistor array into slot ‘R2’

## Slide 64: You may bend the two far pins on reverse side so that part doesn’t fall out while soldering.

## Slide 65: Solder the pins on the resistor array.

## Slide 66: Locate the 2 metal film polarized capacitors

## Slide 67: Polarized Capacitors are orientation critical. The bold white stripe on one side indicates the Negative (minus) side. The Negative side also has a shorter wire

## Slide 68: Locate the Capacitor marked as 100uf (microfarad)

## Slide 69: Place the 100uf capacitor in spot C4. The short lead is the negative and it goes in the shaded part of the C4 location.

## Slide 70: Solder and cut excess of C4 They call it C4 because the capacitor goes boom if you solder it in wrong! (kinda sorta kidding here but the pop will startle you and the smell will be distasteful)

## Slide 71: Locate the 10uf polarized capacitor. Place it in the spot marked C1. The short lead is the negative and it goes in the shaded half of C1 on the PC board.

## Slide 72: Solder and cut excess of C1

## Slide 73: Locate the two tactile momentary switches

## Slide 74: Note how spacing is different between pins

## Slide 77: I usually straighten the legs with a pair of needle nose pliers to make board insertion easier, but it is not required to do so, just use caution

## Slide 78: Insert one switch into position “S1”

## Slide 79: Solder in the first switch

## Slide 80: Repeat with the second momentary switch.. It goes just to the right of the first one in spot S2

## Slide 81: Your board should look like this on top….

## Slide 82: Locate the Power Supply Terminal

## Slide 83: Insert the terminal into spot “J1” Ensure the open sides are facing out as seen here

## Slide 84: Solder in the terminal connection

## Slide 85: Locate the buzzer / speaker

## Slide 86: Place the buzzer in spot U2. The sticker on top indicates the polarity as well as a “+” sign on the side of body. Orientate accordingly. It will not mount flush – do not force

## Slide 87: Solder the two pins on the buzzer. Again, it will not fully seat on board. Do not force it.

## Slide 88: Locate the digital display

## Slide 89: Remove display from foam and straighten legs with needle nose if needed

## Slide 90: Place display onto PC board with the decimal points to the bottom as seen here..

## Slide 91: Solder the display in

## Slide 92: Locate the integrated circuit / IC chip. Note the indent on left side with the dimple on the bottom left. This is “Pin One” and placement is critical.

## Slide 93: Place the IC into the IC Socket with ‘Pin One’ to the left – next to R1. Do Not Push in until you are certain all pins are aligned properly

## Slide 94: Uh-Oh! Who has spare parts??

## Slide 95: Locate battery holder and strip about 3/16” of insulation off the red and black wires. Insert the red wire to the + positive terminal and tighten with Phillips head screwdriver. Insert the black wire to the negative ‘GND’ terminal and tighten.

## Slide 96: If no-one has checked out your clock, please allow one of us to do so before putting in batteries! - Just to be safe

## Slide 97: Insert the two AA batteries. Refer to directions on how to program!